## Slide 1: Full-bar Signal: A Wi-Fi AP Positioning System App
Done by:
Sewar Gharaibeh
Rufaida Altalahmeh
Nagham Al-Zoubi
Aya Al-Antari
Supervised by:
Dr. Ahmad Al-Hammouri
Dr. Fahed Awad
Network Engineering and Security Jordan University of Science and Technology

## Slide 2: Outlines
Introduction
Smart WiMAP Tool: A brief history
Smart WiMAP vs Full-bar Signal
Full-bar Signal Application Process
Testing
  Throttling
  Scanning Test
  Full-bar Signal and Smart WiMAP Test
Demonstration
Conclusion

## Slide 3: INTRODUCTION
What is Full-Bar Signal?
- Optimal AP locator
- Written in Java
- Supports most Android devices
- Easy steps
- Generates heatmap

## Slide 4: Smart wImap: a brief history
Unix-based tool, written in Java
AP locater
Heatmap generation
Rogue AP detection

## Slide 5: Smart WiMAP vs Full-bar Signal
 | OS | Tool goal | Scanning Method
Full-bar Signal | Android | Finding the optimal AP location | Active Scanning
SMART WIMAP | Linux | Showing the coverage heatmap | Passive Scanning

## Slide 6: Active scanning VS passive scanning
Active scanning :
The device initiates the scan
  Advantages
    More accurate results
    User Control
  Disadvantage
    Increased power consumption
    Increased Network Traffic
Passive scanning:
The device acts like listener
  Advantages
    Lower power consumption
    Faster scan time
  Disadvantage
    The device needs to be rooted in Android

## Slide 7: Full-bar Signal APPLICATION PROCESS
Main Activity
MAP Activity
Heat MAP Activity

## Slide 8: FULL-BAR SIGNAL APPLICATION PROCESS
MAIN ACTIVITY​
Scanning network information​
Choose user's AP​

## Slide 9: FULL-BAR SIGNAL APPLICATION PROCESS
MAP ACTIVITY
UPLOADING MAP IMAGE
TAKING THE REQUIRED NUMBER OF SAMPLES
CALCULATING ENVIRONMENT CHARACTERISTICS PARAMETERS
  N(PATH LOSS EXPONENT) AND SIGMA(SIGNAL VARIATION)
CHOOSE OPTIMAL AP LOCATION BETWEEN GIVEN SUGGESTIONS

## Slide 10: FULL-BAR SIGNAL APPLICATION PROCESS
Heat MAP Activity.
Show heat map for all suggested location.

## Slide 11: THROTTLING
It involves restricting the frequency of Wi-Fi scanning to enhance network performance, improve security, and extend battery life.
It is evident that the utilization of throttling results in a higher number of scans conducted and an increased scan rate, as compared to the scenario without throttling.
Device Type | Android Version | Scanning Time | Total Scans |  | Scan Rate (scan/s) | 
 |  |  | Throttling ON | Throttling OFF | Throttling ON | Throttling OFF
Samsung Galaxy A53 | 13.0 | 10 minutes | 24 | 186 | 0.02 | 0.31
Samsung Galaxy A7 | 10.0 | 10 minutes | 27 | 452 | 0.04 | 0.75
Below is a table illustrating the contrast in scanning rates when Throttling is enabled and disabled.

## Slide 12: SCANNING TEST- part1
Group # | Device Type | Android Version | Scanning Time | Scan Number | Scan Rate
Group 1 | Samsung A53 time1 | 13 | 10 min = 600 sec | 186 | 0.31/sec
 | Samsung A7(1) time1 | 10 | 10 min = 600 sec | 452 | 0.75/sec
Group 2 | Realme 8 | 12 | 5 min = 300 sec | 1435 | 4.78/sec
 | Samsung S21 | 13 | 10 min = 600 sec | 791 | 1.31/sec
Group 3 | Samsung A52 | 13 | 5 min = 300 sec | 138 | 0.46/sec
 | Samsung S21 | 13 | 5 min = 300 sec | 278 | 0.93/sec
Group 4 | Samsung A31 | 12 | 5 min = 300 sec | 5770 | 19/sec
 | Infinix HOT12 time1 | 12 | 3 min = 180 sec | 2779 | 15.4/sec
 | Infinix HOT12 time2 | 12 | 5 min = 300 sec | 5215 | 17/sec
Group 5 | A7(1) time2 | 10 | 4 min = 240 sec | 168 | 0.7/sec
 | A7(2) time2 | 10 | 4 min = 240 sec | 191 | 0.79/sec
The table below illustrates the close rates observed across devices within a shared environment when the Throttling option is turned off. Each group of devices represents the testing process conducted in the same environment.

## Slide 13
SCANNING TEST- PART2
We tested the same seven devices on one AP in the university library and the scan rate was nearly identical. It ranges from one scan/sec to 1.5 scan/sec.
The investigation on using Wireshark on monitor mode
When testing in monitor mode using (for loop and throttling off) .The time between the probe requests is around one second.

## Slide 14
SCANNING TEST- PART2 cont.
And the time between the probe request and reply is around 0.004/sec
We solve this problem (different scan rates) by making the user stand in the same point until we gather the required number of samples.

## Slide 15: EFFECT OF THE NUMBER OF SAMPLES AND AP PLACEMENT
AP Location --> in the corner of the testing area
# of samples --> 19 samples
Result: path loss exponents (n) equal 1.64
Test 1

## Slide 16: EFFECT OF THE NUMBER OF SAMPLES AND AP PLACEMENT cont.
AP Location --> at the center
# of samples --> 53 samples
Result: path loss exponents (n) equal 2.27
Test 2
The expected range of the "n" value in the "Obstructed in building" about 4 to 6.

## Slide 17: TESTING RESULTS
The outcome of the testing conducted at the CH building within JUST University is as follows:
 | Smart-WiMAP | Full-bar Signal | Error Percentage
Map Scale (meters: pixels) | 1: 88 | 1: 74 | 15.9 %
Path Loss Exponent (n) | 2.53 | 2.32 | 8.3 %
Greater accuracy in the Smart-WiMAP due to:
finger thickness
  Mouse clicks for selection when selecting two points on the map to enter their real distance in meters, whereas the Full-bar Signal relies on finger taps.
Average RSSI:
  Smart-WiMAP tool takes an average of 10 RSSI readings, the full-bar signal application takes the average of only 3 RSSI readings due to its scanning limitation capabilities in active scan.

## Slide 18: DEMo

## Slide 19: Conclusion - Future Work
Full-bar Signal mobile application:
Incorporate INS (Inertial Navigation System) for improved indoor positioning.
Add zoom in and out functionality to enhance map viewing options.
Enhance the user interface for improved usability.
Develop the ability to find optimal locations for multiple access points (APs).

## Slide 20: THANK YOU!